## Slide 1: WORKSHOP I: Green Infrastructure Overview and Maintenance
Stormwater BMP Maintenance – Osterville Library
11.8.17

## Slide 2: WHY IS THIS IMPORTANT?
STATE AND LOCAL AGENCIES
DESIGNERS
CONTRACTORS
OWNERS & OPERATORS
CONSTRUCTION DRAWINGS
INSTALLATION
REGULATIONS AND DESIGN MANUALS
OPERATION AND MAINTENANCE

## Slide 4
HOW CAN WE AVOID THIS?
1 Drainage Inlets
2 Swales & Conveyance
3 Sediment Capture
4 Treatment Areas
(Bioswales/Raingardens)
5 Overflow & Spillways
6 Surrounding Area
Vegetation
Long-Term Maintenance
Notes: Why proper installation/materials are important
Importance of maintenance

## Slide 5: 1 DRAINAGE INLETS
Diversion struct.
Pipe Inlets
Trench grates
Curb Cuts
Paved inlet flumes
Catch basins
Roof downspouts
Notes: Why proper installation/materials are important
Importance of maintenance

## Slide 6: MAINTENANCE
Clean sediment
Remove leaf litter from inlets
Watch for scouring
Inlet Clogging

## Slide 7: LESSONS LEARNED
Stones prone to clogging
Ensure it is located at the low point and water can enter easily.
Curbing increases side slope and depth
When applicable zero curb
  Allow for sheet flow

## Slide 8: 2 SWALES & CONVEYANCE
Grass swales
Vegetated swales
Turf reinforced (TRM) swales
Stone swales
Notes: Why proper installation/materials are important
Importance of maintenance

## Slide 9: MAINTENACE
Debris Cleanout
Sediment/Organic Debris Removal
Check for areas of erosion/ gullies in the swale, particularly along the swale bottom.
Repair/reseed as necessary
Overtopped berm

## Slide 10: 3 SEDIMENT COLLECTION
Notes: Why proper installation/materials are important
Importance of maintenance

## Slide 11: MAINTENANCE
Remove trash and debris from the surface.
Signs of erosion gullies. Repair as necessary.
Remove sediment accumulation and properly dispose when accumulation is greater than or equal to 3 inches or you cannot see stones.*

## Slide 12: LESSONS LEARNED
Early Designs
    Inlets & Sediment collection areas or “forebays” with rip/rap or stone
    Sediment forebays large/difficult to clean
    Lessons Learned
  Smaller forebay/more frequent cleaning
  Use a hardscape smooth surface at the bottom
Notes: Aha moment - Spend time during construction trying to keep sediment out at the inlet. Why nor design this way with more frequent cleaning
Stone at inlet set too high- traps sediment at the paved flume. Incorrect installation, but why not design to trap sediment before entering the treatment area.

## Slide 13: 4 TREATMENT AREAS
Notes: Why proper installation/materials are important
Importance of maintenance

## Slide 14: MAINTENANCE
Debris Cleanout
Signs of erosion gullies, animal burrowing, overtopping or slumping
Sediment/Organic Debris Removal
Vegetation Maintenance & Replacement
Water Draining properly
  If standing water is observed for more than 48 hours after a storm event maintenance required

## Slide 15: LESSONS LEARNED
Early Designs
  6”-12” depth
  Flat bottom – zero slope
  Became too deep
  Side slope stabilization
  Curb and gutter systems
Lessons Learned
  Shallower depth has advantages
  Use check dams
  More cells
Benefit
  Aesthetics
  Improved Function
  Easier Maintenance
Source: Los Angeles Zoo designed by others

## Slide 16: 5 OVERFLOW & SPILLWAYS
Overflow/Outlet Structures
Spillways
Notes: Why proper installation/materials are important
Importance of maintenance

## Slide 17
MAINTENANCE
EMERGENCY SPILLWAYS
  Check for settling gulling, erosion damage, settling & clogging
  Repair as necessary and return to design grades
OVERFLOW STRUCTURE
  Check for sediment accumulation that impacts inflow. If sediment accumulation. Schedule cleaning
  Check for leaf litter, debris and inlet clogging

## Slide 18: 6 SURROUNDING AREA
Debris Removal
  Remove trash from perimeter areas.
Pavement Sweeping
  Sweep parking lot minimum once a year after spring thaw.
Drainage Network
  Ensure proper operation.
Contributing drainage area stabilized
Notes: Why proper installation/materials are important
Importance of maintenance

## Slide 19: VEGETATION
Pruning
  Why?
    Maintain plant health and vigor
    Removal of dead or broken wood
    Encouragement of flowering and fruiting
    Control of overgrowth of plant material
  When?
    Annually – Fall or Spring
Weeding
Why?
  Control invasive plants
  Promote native non-invasive plant growth
When?
  Monthly
  April thru October
Do not use chemical herbicides
Remove by hand
Notes: 10:00 – 10:30 GI Maintenance Activities (4 slides)
Vegetation management and maintenance – importance of plant lists and understanding native plants vs. invasives

## Slide 20: VEGETATION
Notes: 10:00 – 10:30 GI Maintenance Activities (4 slides)
Vegetation management and maintenance – importance of plant lists and understanding native plants vs. invasives

## Slide 21: LESSONS LEARNED
Early Designs
  Ornamental/flowering “gardens”
  Predominantly Native Plants
  Included Larger shrubs
  Trees often excluded
  Lessons Learned
  Greater mix of plants
  Grasses, Herbs and Forbs do
  well
  Less manicured and ornamental more wild & natural
  Work with Nature
Source: SW Montgomery Green Street Plan by Nevue Ngan
Notes: Is weedy/unkept and option?
Do a better job managing expectations
Changing people’s perspective/habitats

## Slide 23
SMART WEED

## Slide 24
ORIENTAL BITTERSWEET
JAPANESE KNOTWEED

## Slide 25: TO MOW OF NOT MOW?
THAT IS THE QUESTION ?

## Slide 26: FERTILIZING
Fertilization should not be necessary
  Compromises pollutant reduction effectiveness
  Leads to weak plant growth
  Promotes disease and pests
  Inhibits soil life

## Slide 27: SHORT-TERM MAINTENANCE
Why Inspect?
  Ensure proper design function after construction
When to inspect?
  6 months period after construction
  Monthly during an immediately after construction
  After rain events of 1” and greater
What to inspect?
  Erosion and Gullying
  Grass/Plant growth
  Washouts Inlet flumes or pipes inlets
  Sediment forebay
Notes: 10:00 – 10:30 GI Maintenance Activities (10-12 slides)
Typical routine and long-term maintenance measures

## Slide 28: LONG-TERM MAINTENANCE
When to inspect?
  Spring thru fall
  During the typical routine landscape maintenance:
  Once per month
  After large storm events
  During other extreme weather events
What to Inspect?
  Debris Accumulation
  Sediment build up
  Weeds and invasive plants
  Plant and grass health
  Erosion/Gullying
  Inlet/Outlet structure clogging

## Slide 29
How Do They Work?

## Slide 30
Stormwater
Pretreatment
Buffer Restoration
Pavement Reduction
SITE 12

## Slide 31: SITE 3b

## Slide 35
THANK YOU!
QUESTIONS?

## Slide 36: HANDS-ON MAINTENANCE EXERCISE
10:45 – 11:45 Hands-on Maintenance Exercise
Visit the rain garden at the library
Visit the swale in the back of the parking lot